## Slide 1: Kip kop network
Ocskó Gábor, Jelenovics Milán, Kómár Attila

## Slide 2: IP address allocation (VLSM)
Ocskó Gábor

## Slide 3: What was the task?
• Network identifier - both in binary and decimal form
• Scatter address - both in binary and decimal form
• First assignable IP address - in both binary and decimal form
• Last assignable IP address (If the network contains switches, they will receive the last assignable IP address) - in both binary and decimal form
• Second assignable IP address (If the network contains servers, they will receive the second assignable IP address) - in both binary and decimal form
• Subnet masks - binary, decimal and prefix
• Total cost of all IP addresses to be purchased

## Slide 4: Implementation
-create an empty vlsm table
-put the ip addresses in the right place
-arrange to be transparent (optional)
-Use the DEC.BIN command to convert what was needed to binary
calculate how bad the forint is, that is, calculate how much it will cost

## Slide 6: Creating the network topology
By Jelenovits Milán

## Slide 7: Routers, Switches
Router(2911): Adding network cards (HWIC-1GE-SFP) for Gigabit Ethernet ports (GLC-LH-SMD)
Switch(PT-Empty): Adding Gigabit Ethernet ports(NM-1CGE)

## Slide 8: Computers, printers
Replacing network cards from Fast Ethernet (100 Mbps) to Gigabit Ethernet cards

## Slide 9: Google Cloud
1 Switch (2960), 1 DNS Server

## Slide 10: Google network and DNS configuration
Kómár Attila

## Slide 11: Server IP configuration
IP address: 8.8.8.8
Mask: /16 (255.255.0.0)
Default gateway: 8.8.0.1
DNS Server’s IP is itself

## Slide 12: DNS (Domain Name System)
Turn the DNS Service on
Website’s name: gdprojekt.net
Address: 185.62.128.1

## Slide 13: R_BP Router configuration
enable
configure terminal
ip route 0.0.0.0 0.0.0.0 GigabitEthernet0/0
interface GigabitEthernet0/0
ip address 8.8.0.1 255.255.0.0
no shutdown
exit

## Slide 14: Budapest-net network configuration
Ocskó Gábor

## Slide 15: What did you have to do?
On the switch:
-set password in privileged EXEC mode
-add a username and password
-remote access with telnet
-set login message
-config to the tftp server
On the router:
-set password in privileged EXEC mode
-enter username with password
-remote access with ssh

## Slide 16: Implementation the commands on the switch

## Slide 17: Implementation the commands on the router

## Slide 18: Webpage
By Jelenovits Milán

## Slide 19: Copying source

## Slide 20: Text layout
Arrangements of paragraphs, lists and links
List
Paragraph
Link

## Slide 21: Style
Background, Resizing image, Text indent and font size

## Slide 23: Kecskemét-net network
By Jelenovits Milán

## Slide 24: Topology

## Slide 25: IP addresses
PC-K1: 185.62.128.132
PC-K2: 185.62.128.133
PC-K3: 185.62.128.134

## Slide 26: SW Kecskemét configuration

## Slide 27: Szolnok Wifi subnet configuration
Kómár Attila

## Slide 28: Topology

## Slide 29: IP addresses
Printer: 192.168.10.2
PC: 192.168.10.3

## Slide 30: Wifi Setup

## Slide 31: Wifi Wireless

## Slide 32: Wireless devices

## Slide 33: I, K, S and O networks
Ocskó Gábor

## Slide 34: The topology

## Slide 35: What was the task?
-To set the ip addresses of R-SZOLNOK
-Set a password and set a message of the day
-Save config to tftp server

## Slide 36: R-SZOLNOK
To set the ip address and the other stuff listed, you needed these:

## Slide 37: Checking the network
P A I N

## Slide 38: What was the task?
-Check with the courier
-To ping
-Is the Gdprojekt.net page available?
-Ssh and telnet

## Slide 39: Mail and ping

## Slide 40: gdszeged.net from the szeged pc

## Slide 41: SSH and Telnet
ssh also requires a user, but telnet only requires an ip address

## Slide 42: Thank you for your attention!